## Slide 1: Numerical Solution Configuration & Diagnostics

## Slide 2: Recap: the discretized flow equation

## Slide 3: Picard iteration

## Slide 4: Linear Solution methods

## Slide 5: MODFLOW program flow chart

## Slide 6: IMS basic settings
Non-Linear (Picard)
  Maximum outer iterations
  Outer dvclose (<= inner dvclose)
Linear
  Linear accelerator (CG, BICGSTAB)
  Maximum inner iterations
  Inner dvclose
  Inner rclose
    Infinity norm (max residual)
    Infinity norm – strict
    L2-norm
    Relative based on L2-norm
IMS file:

## Slide 7: IMS preconditioner settings
Incomplete LU factorization
  Zero-fill (ILU0) – preconditioner_levels = 0
  Level-fill (ILUT) – preconditioner_levels > 0
  Drop tolerance – preconditioner_drop_tolerance > 0
  Relaxation factor – relaxation_factor > 0.0
https://doi.org/10.48550/arXiv.1308.5215
IMS file:

## Slide 8: IMS miscellaneous linear settings
number_orthogalizations – recalculate residual from A and b rather than updating using solver coeffcients
scaling_method
  none
  diagonal
  L2-norm
reordering_method
  none
  reverse Cuthill McKee ordering (rcm)
  Minimum degree (md)
Darure (2017)
IMS file:

## Slide 9: IMS non-linear convergence options
Pseudo transient continuation (PTC)
  Newton-Raphson
  Steady-state stress periods
Under-relaxation
  Simple
  Cooley
  Delta-Bar-Delta
Backtracking

## Slide 10: IMS non-linear convergence options (cont.)
Newton under-relaxation
  Limit dependent-variable changes between consecutive nonlinear iterations in model cells and reduce the occurrence of dependent-variable values below the bottom-most elevation of a flow model
  Defined in the model name file options block

## Slide 11: Getting started with IMS
Start with:
  complexity = simple
  default settings for IMS variables
  relaxation_factor = 0.97
  Groundwater problems with a lot of heterogeneity may need more inner iterations (inner_maximum) than the default value of 50